## Slide 1: IPLIB OVERVIEW
Presentation By,
Sharath Manjunath

## Slide 2: IPLIB Creation
ipLibSetOutTbl() will call ipLibBothSideStart(). ipLibBothSideStart() will call ipLibSetLibInfS() to decide the sort order of the output table.
ipLibMakeFront() and ipLibMakeBack() for the front and back page info to be updated. Later ipLibSetOutTblPage() function is called which checks the condition either to print F2B or B2F and based on that values are updated in the OutDump.

## Slide 3: Insert, Cover, Interleave
ipLibGetInputPageAtr() is responsible for the page like cover both front and back, Insert pages. Which gives necessary information of the page and its attributes and updates it with the job being performed and modifies according to it.
First it will check IPLIB_PAPER_NORMAL, If not then IPLIB_PAPER_FCOVER and IPLIB_PAPER_BCOVER are checked and the values are updated accordingly.

## Slide 4: 1. Duplex cancellation based on paper size/Type
The paper can be duplexed only if it is in the below range and needs to satisfy both.
1. Width – Min(140mm) and Max(297mm)
2. Length – Min(182mm) and Max(432mm)
Envelope papers cannot be duplexed, because it may holds good in either width or length but not both.
Duplex is done for all standard size papers.

## Slide 5: 1. Cont…. Macros
These macros have been defined in an header files to check whether the duplex can be made or not.
  #define IPLIB_LENGTHMIN 182mm
  #define IPLIB_LENGTHMAX 432mm,
  #define IPLIB_WIDTHMIN 140mm
  #define IPLIB_WIDTHMAX 297mm
This macros have been added in ipLibDuplexTbl which will also contains macros for custom paper sizes also.

## Slide 6: 1. Cont.… Code Flow…! 
ipLibChkDupSize() refer to ipLibDuplexTbl macros and decide whether duplex can be done or not.
How to get Job Done??
--- Give the Condition with respect to the combination of MIN and MAX macro and Enjoy the Result.
If the Condition is not satisfied, the job will be converted to Simplex.

## Slide 7: Question arises: How it will convert to simplex??
RIP will send ESFC message with value assigned to hSingleSide variable. Based on this value IPLIB will decide whether it can be duplexable or not.

## Slide 8: Will the paper types effect for duplexing??
Yeap it will effect.
ipLibChkDupMedia() is responsible for duplexing based on paper types.
Depending on the machine, the paper types are supported for duplexing.
All the possible paper types have been defined in cpyCheckSuppotedMediaType().

## Slide 9: 2. Remake Mechanisms
JobSkip - iSeqNo value will reset so it is required to set the hLastSeqNumber value to ‑1.
Sharath Fix the issue 
When the stack size changes[ Custom Duplex]. When tolerance comes into the Picture.

## Slide 10: Remake Mechanism
Explain JobSkip??
Stack size for duplex varies from MFP to MFP.
Note:
ipLib_StkMaxFlag will be set to 3 for shasta/Shastina and 2 in Weiss/Reuss.
ipLibCustomStkSizeCheck() will be called for special paper types.
ipLibCustomStkSizeCheck() will be updated with hStkMax value ipLibBothSideEnd() will be called.
ipLibBothSideStart  Push the pages
ipLibBothSideEnd  Pop the pages.

## Slide 11: Question Arises: If 1st page is A4 and 2nd Page is A3, Can be duplexed??
ipLibCheckPattern() will compare the current page size and previous page size. If both pages are same, then "hPatternFlag" will be returned as 0 and paper is duplexable.
What if not??
hPatternFlag – 0  Present
1 Check for an entry
2If no entry moved to exit tray.
3 End of Input Table.

## Slide 12: You Forgot the Main Point: When RJRM Comes into Picture w.r.t Stack???
If length exceeds more than or equal to 216mm because of tolerance.
RJRM thrown and IPLIB will Update the Input and Output table.
prnEx will send IPLIB_REMAKE_MIDDLE.
If not able to Duplexable with the updated values then RJRM will be thrown with IPLIB_REMAKE_DUPLEX_CANCEL.